Sandbox
Dan Walsh
Red Hat, Inc.
<dwalsh@redhat.com>

---
What is a sandbox
- Run general applications in a locked down environment.
  - Less privileged then other processes run by the user.
  - Block Networking
  - Block Access to other Processes
  - Block Access to files, homedir?
  - Block Access to resources like X, dbus
- Run untrusted applications or filters on untrusted data.

---
What is SELinux
sandbox?
- Two Sandbox in one
  - Simple sandbox allows process access to stdin/stdout/and other passed in file descriptors
  - Read/Execute on all other apps.
- X Sandbox
  - Replace $HOME and /tmp
  - Use Different X Server
  - Lock down by SELinux
    - NO setuid, No Network, No access to user content

---
What is new in F13/RHEL6?

---
CGROUP Integration
- sandbox -C
- /etc/sysconfig/sandbox
  - CPUAFFINITY - cpus that all sandboxes will run on
    - Values ALL (default) or comma-separated Ex: 0-2,5
  - MEMUSAGE – Total memory for sandboxes
    - 80% (default) – Or specify use suffixes (K, M, G) 100M
  - CPUUSAGE – Total cpu percentage for sandboxes
    - 80%(default)
  - Future rlimits values (Number of processes) when cgroups supports them.

---
SELinux context optional
- Seunshare – setuid tool used to setup sandbox
  - Run sandboxes under standard current context
  - Run sandboxes on machines with SELinux disabled
    - Cgroup
    - Namespace replacement of $HOME and /tmp
  - seunshare [ -v ] [ -t tmpdir ] [ -h homedir ] [ -Z context ] -- executable [args]

---
Entire Desktop session
- sandbox -S
  - MLS Desktop
    - Full separation without problems of Xace
    - Simpler configuration
    - Future integration into gnome-shell?
  - Alternate desktops for security
    - Online Banking desktop
    - Gaming Desktop
- Problems:
  - Really need a way of saying which apps run within desktop

---
Resizable X Server
- Thomas Liu – rewrote a patch to allow Xephyr xservers to be resizable

---
Discussion?